PART A : Pre Requisite Documentation Test
Write a brief documentation on what prerequisite things need to be checked (hardware and software checks) before starting to do a mapping or navigation task.

In order to have a proper mapping and navigation task, we need several checks for both hardware and software side as below :

- Hardware
  - Robot plaform
    - Ensure all the robot platform is assembled properly, such as joints of the robot
    - Ensure the supply power for the robot is sufficient for the task
  - Sensor
typically in navigation stack, we use several sensors like LIDAR/Depth camera, IMU, and encoders.
    - LIDAR/Depth camera: check if the LIDAR or Depth camera are properly mounted, connected, and calibrated.
    - IMU: ensure the IMU is calibrated and functioning.
    - Encoders: Verify the feedback (tick or count) are providing accurately.
  - Computer
    - Ensure the computer functioning properly and has sufficient processing capability to handle all the sensors and running the navigation stack.
  - Networking
    - Verify that all necessary network connections (wired or wireless) are stable and operational to ensure communication between different components (sensors, robot, remote monitoring). Such as address, ports, comms, and so on.

- Software
  - Operating system and ROS version
    - Ensure OS of ubuntu and ROS are in correct version specifically for our system’s needs
  - packages
    - Ensure that all required ROS packages for the navigation stack are installed, including gmpping, navigation, amcl, move_base, and any sensor-specific drivers that our system use.
  - Configuration
    - Verify that all configuration files (YAML, launch files) are properly set up for the robot's specific hardware and software configuration.
    - Ensure that the robot's URDF (Unified Robot Description Format) file is accurate and properly describes the robot's physical properties.
  - Topics
    - Verify that the topics for sensor data (e.g., /scan for LIDAR, /camera/depth/points for depth camera) are correctly published and accessible.
    - Use ROS tools like rostopic list and rviz to visualize and confirm the integrity of the sensor data streams.
  - TF Tree
    - Ensure that the TF (transform) tree is correctly set up and broadcasting the necessary frames (e.g., base_link, odom, map).
    - Use roswtf and tf view_frames to diagnose and visualize the TF tree.
- Robot testing
  - Control with teleoperation
    - Ensure that the robot can move with corresponds to the teleoperation that publishes /cmd_vel. We can use ROS CLI to publish cmd_vel topic or running the node by using :
          rosrun telelop_twist_keyboard teleop_twist_keyboard.py
    - Check also both linear and angular velocity. We can calculate it with distance traveled divided by time. For ensuring constant velocity from the start, use publish CLI instead of teleop_twist_keyboard package.
    - Check the odometry by comparing /odom topic and distance traveled if the odometry meets the minimum tolerance/offset.
    - Check if the robot move in a straight line. We can draw a line in the floor to easily check it.

PART B : Programming Test
Program a waypoint-following node that would follow a series of 5 waypoints on known areas only. You may define the points as you like, though we would prefer a complicated route.
You can develop with the help of planners and controllers already available in ROS.
Test at least with 2 different controllers -
We expect proper documentation on how you tuned the parameters, pros and cons of the controller used.

To setup the environment, I use the following package:

https://github.com/pikkuri14/ros_motion_planning.git

Set all the environment using readme that is provided by the repository. For setting up accordingly the host machine environment, use README.md, for docker deployment use docs/docker.md, and for launching waypoint use docs/waypoint.md

There are a bunch of planners and controllers inside the package. As of this test, we are going to use A* for the planner, dynamic windows approach (DWA) and Proportional Integral Derivative (PID) for controllers.

Before tuning the controllers, I usually pay attention to localization parameters also (i.e amcl package). Its key parameters would be "laser_z_hit" and "laser_z_rand". Those parameters basically saying how much do we trust to the map.

As general planners and controllers. We need to adjust the inflation radius. By inflating the area around obstacles, the robot is less likely to come into contact with them, reducing the risk of collisions and avoding the path planners to plan near that obstacle.

- DWA controller tuning
  - "sim_time" :
    A higher sim_time increases computational load and results in longer, less flexible paths. A lower sim_time may not allow the planner to find optimal trajectories through narrow passages.
    Around 4.0 seconds for high performance; avoid values below 2.0 seconds or above 5.0 seconds
  - "vx_samples" "vy_samples" "vth_samples"
    More samples increase computation but can improve path quality. Rotational velocities usually require more samples than translational
  - Trajectory Scoring Weights "path_distance_bias", "goal_distance_bias", "occdist_scale"
    - path_distance_bias: Higher values make the planner stick closer to the global path.
    - goal_distance_bias: Higher values make the robot prioritize reaching the goal over following the global path precisely.
    - occdist_scale: Higher values increase the robot's tendency to avoid obstacles, which might lead to indecisiveness.
  - Goal tolerance "yaw_goal_tolerance", "xy_goal_tolerance" : Define how close the robot needs to get to the goal before considering it reached
- PID controller tuning
  It is common to start with tuning the proportional gains (k_v_p and k_w_p), followed by the derivative gains (k_v_d and k_w_d) to improve stability, and finally the integral gains (k_v_i and k_w_i) to eliminate any steady-state errors.
  PID (Proportional-Integral-Derivative) Controller
Pros:
- Simplicity: Easy to understand and implement.
- Smooth Control: Provides smooth and gradual adjustments.
- Real-time Performance: Low computational overhead.
Cons:
- Limited Adaptability: Struggles in dynamic environments.
- Manual Tuning: Requires time-consuming manual adjustments.
- Lacks Path Planning: Not suitable for complex navigation scenarios.
DWA (Dynamic Window Approach) Controller
Pros:
Dynamic Path Planning: Adapts to real-time and dynamic obstacles, can perform collision avoidance.
Cons:
- Computationally Intensive: High resource requirements.
- Complexity: More difficult to implement and tune.
### When to Use
- PID: For predictable paths, smooth control, simpler systems.
- DWA: For dynamic environments, real-time obstacle avoidance, complex navigation tasks.

PART C : Algorithmic Test
Attached is a rosbag file containing a recorded path for a robot. This path is used as waypoints for a robot path-following algorithm. The issue is, as you can see, there are almost 1000 points in this path, which could be too much for the path following algorithm to handle.Your task is to simplify this path, which means to reduce the number of points in the path, while keeping the shape of the simplified path as close to the original as possible. Assume also that the given path contains some noise that you must mitigate. Write a Python program that takes the given rosbag file as an input, and outputs a new path with N points, where N is the number of points in the new path. The program should allow us to adjust the parameter N.

The algorithm is located in src/task/scripts/visualize.py. The filtering algorithm uses downsampling method, the N points that we want can be configure inside the program. Use docs/pose_filtering.md to launch the program