PART A : Pre Requisite Documentation Test
Write a brief documentation on what prerequisite things need to be checked (hardware and software checks) before starting to do a mapping or navigation task.

In order to have a proper mapping and navigation task, we need several checks for both hardware and software side as below :

- Hardware
  - Robot plaform
    - Ensure all the robot platform is assembled properly, such as joints of the robot
    - Ensure the supply power for the robot is sufficient for the task
  - Sensor
typically in navigation stack, we use several sensors like LIDAR/Depth camera, IMU, and encoders.
    - LIDAR/Depth camera: check if the LIDAR or Depth camera are properly mounted, connected, and calibrated.
    - IMU: ensure the IMU is calibrated and functioning.
    - Encoders: Verify the feedback (tick or count) are providing accurately.
  - Computer
    - Ensure the computer functioning properly and has sufficient processing capability to handle all the sensors and running the navigation stack.
  - Networking
    - Verify that all necessary network connections (wired or wireless) are stable and operational to ensure communication between different components (sensors, robot, remote monitoring). Such as address, ports, comms, and so on.

- Software
  - Operating system and ROS version
    - Ensure OS of ubuntu and ROS are in correct version specifically for our system’s needs
  - packages
    - Ensure that all required ROS packages for the navigation stack are installed, including navigation, amcl, move_base, and any sensor-specific drivers that our system use.
  - Configuration
    - Verify that all configuration files (YAML, launch files) are properly set up for the robot's specific hardware and software configuration.
    - Ensure that the robot's URDF (Unified Robot Description Format) file is accurate and properly describes the robot's physical properties.
  - Topics
    - Verify that the topics for sensor data (e.g., /scan for LIDAR, /camera/depth/points for depth camera) are correctly published and accessible.
    - Use ROS tools like rostopic list and rviz to visualize and confirm the integrity of the sensor data streams.
  - TF Tree
    - Ensure that the TF (transform) tree is correctly set up and broadcasting the necessary frames (e.g., base_link, odom, map).
    - Use roswtf and tf view_frames to diagnose and visualize the TF tree.
- Robot testing
  - Control with teleoperation
    - Ensure that the robot can move with corresponds to the teleoperation that publishes /cmd_vel. We can use ROS CLI to publish cmd_vel topic or running the node by using :
          rosrun telelop_twist_keyboard teleop_twist_keyboard.py
    - Check also both linear and angular velocity. We can calculate it with distance traveled divided by time. For ensuring constant velocity from the start, use publish CLI instead of teleop_twist_keyboard package.
    - Check the odometry by comparing /odom topic and distance traveled if the odometry meets the minimum tolerance/offset.
    - Check if the robot move in a straight line. We can draw a line in the floor to easily check it.

PART B : Programming Test
Program a waypoint-following node that would follow a series of 5 waypoints on known areas only. You may define the points as you like, though we would prefer a complicated route.
You can develop with the help of planners and controllers already available in ROS.
Test at least with 2 different controllers -
We expect proper documentation on how you tuned the parameters, pros and cons of the controller used.

To setup the environment, I use the following package:

https://github.com/pikkuri14/ros_motion_planning.git

Clone the repository by execute command below :

git clone https://github.com/pikkuri14/ros_motion_planning.git

Set all the environment using readme that is provided by the repository. For setting up the host machine environment, use README.md, for docker deployment use docs/docker.md, and for launching waypoint use docs/waypoint.md